## Slide 1
Introduction
Determining the Practical Range of Bluetooth Low Energy on an iPhone and a Raspberry Pi
Purpose
With the beginnings of smart appliances around the home, technology such as Bluetooth Low Energy is becoming more important than ever, but little is known about its range. This experiment was designed to determine the practical range of Bluetooth Low Energy both inside and outside.
Hypothesis
*
*
Conclusions
Methodology
Results
Results Cont.
A Raspberry Pi using a Low Energy Bluetooth USB nub will be able to detect nearby devices from a distance no greater than 40 feet.
The first step in determining the practical range was to establish a baseline and determine whether the direction of the Bluetooth nub mattered. These two were tested outdoors on flat ground. Then the Raspberry Pi was raised to a height of 4 feet, and the experiments were repeated using the ideal orientation of the nub. Placing the Raspberry Pi back on the ground, motion tests were performed by moving in a straight line with the cosest point being the measurement. Lastly, the first test was repeated inside, except with a wall placed between the two devices. It was tested moving each device away from the wall as well as moving both devices.
When first determining the ideal orientation of the Bluetooth nub, it appeared as though 0o was ideal. Although 0o was the strongest, 180o turned out to be most consistent over the longest distance, making it the ideal orientation.
When comparing the height of 0 feet and 4 feet, it became very apparent that a height of 4 feet greatly increased the range. A distance of 80 feet was the farthest that the available setup could test.
With a wall placed between the two devices, very little difference was seen through 15 feet, but at distances greater than 15 feet, the signal was strongest by far when neither device was next to the wall.
Today’s world is booming with new technology from wearables to drones to technology-infused cars. This multitude of technological advances is becoming so ingrained into our daily lives that our world requires a way to wirelessly interconnect them. Bluetooth Low Energy may just be that system, but its practical range remains uncertain in many situations.
The goal in this experiment was to determine the ideal setup for consistently detecting an iPhone using Bluetooth Low Energy and determine its range. When the results from all of the tests are combined, it was determined that the ideal indoor setup consisted of placing the Raspberry Pi at a height of 4 feet away from a wall with the Bluetooth nub facing away from the general location of the iPhone.
Graph 1:
Distance tests at a height of 0 feet, with rotation trials.
Trial A = 0o
Trial B = 90o
Trial C = 180o
Trial D = 270o
Graph 2:
Comparison of each rotation to the 0o trial. Positive values refer to a greater number of times seen.
Graph 3: Outdoor distance tests with the Raspberry Pi at a height of 4 feet.
Graph 4: Outdoor motion trials with the Raspberry Pi on the ground and the iPhone 5 at waist height, at three different speeds.
Graph 5: Indoor trials with a wall between the iPhone 5 and the Raspberry Pi, moving the iPhone 5, Raspberry Pi, and both, respectively.